## Slide 1
Gold Deposit
Drillhole Data Analysis
Geostatistical Study — 94 Drillholes | 4,813 Samples
94
Drillholes
4,813
Total Samples
372
Mineralized Composites
Prepared by: Mohamed | Gold Mining Exploration Analysis | 2026
Notes: Open with the project scope: 94 holes, 4813 samples, full geostatistical pipeline from QC to block model prep.

## Slide 2
Analysis Pipeline
01
Data QC
Validated 94 holes across 4 tables. Identified 35.7% placeholder grades.
02
Desurveying
Minimum Curvature Method — true X,Y,Z for every sample.
03
EDA & Domains
Grade by rock type. IN & QV1 confirmed as mineralized hosts.
04
Directional Analysis
PCA revealed NE-SW trend at 42.7° with 86.5% confidence.
05
Top Cut & Compositing
60 g/t cap applied. 2m domain-aware composites built.
06
Variography
Spherical model: Nugget=18.81, Sill=32.39, Range=218m.

## Slide 3
Phase 1 — Data Quality Control
✓
94 holes validated across all 4 tables
✓
Zero overlapping sample intervals detected
✓
Zero negative gold values
!
35.7% of samples had placeholder grade = 1.00 g/t exactly
!
B rock: 98.8% placeholder → dropped from 99% to 33% economic
!
ST rock: 42.4% placeholder → corrected to 0.58% economic
Notes: Key finding: placeholder grades systematically inflated B and ST rock types. After correction, ST is effectively barren (0.58%).

## Slide 4
Phase 3 — Grade by Rock Type
Chart: Mean Grade (g/t)
| IN | QV1 | MU | B | S2 | ST | SH
Mean Grade (g/t) | 9.15 | 4.14 | 1.95 | 0.7 | 0.42 | 0.1 | 0.08
IN (Intrusive)
9.15 g/t
Highest avg grade
100% economic
QV1 (Quartz Vein)
4.14 g/t
Widest distribution
47 holes
ST (Background)
0.10 g/t
Barren after QC
0.58% economic
Notes: IN and QV1 are the only economic rock types. ST which makes up 70% of samples is effectively barren after placeholder correction.

## Slide 5
Phase 4 — Directional Analysis & Ore Shoot
42.7°
NE-SW Trend
Dominant Azimuth
86.5%
Method
PCA applied to 291 high-grade samples (gold ≥ 3 g/t)
Azimuth
42.7° — consistent in both 2D (plan) and 3D analysis
Confidence
86.5% of spatial variance explained — strong structural control
Plunge
~12° toward SW — shallow, favorable for near-surface mining
Implication
Likely fault or fracture system controlling NE-SW mineralization
Recommendation
Future drilling should target NE-SW corridor extensions
Notes: PCA on 291 high-grade samples reveals a clear NE-SW structural trend. The ore shoot plunges gently SW at 12 degrees.

## Slide 6
Phase 6 — Variogram Analysis
Chart: 
| 24.321999999999999 | 21.777000000000001 | 22.805 | 24.991 | 28.911999999999999 | 33.222999999999999 | 29.524000000000001 | 30.905999999999999 | 34.969000000000001 | 33.829000000000001 | 34.203000000000003 | 25.428000000000001
Spherical Model | 18.81 | 20.67 | 22.51 | 24.27 | 25.95 | 27.5 | 28.89 | 30.09 | 31.08 | 31.81 | 32.25 | 32.39
Nugget (C₀)
18.81
58% of Sill
Sill (C₀+C₁)
32.39
Max variance
Range (a)
218 m
Correlation limit
Model
Spherical
Isotropic
Notes: Range of 218m is the key number for block model search radius. High nugget ratio (58%) confirms short-scale grade variability typical of gold deposits.

## Slide 7
Block Model Inputs — Ready for Surpac / Leapfrog
Parameter | Value | Source
Mineralized Domain | QV1 + IN rocks | Geology + Grade Statistics
Top Cut | 60 g/t | Percentile analysis (P99 = 60 g/t)
Composite Length | 2.0 m | Domain-aware compositing
Total Composites | 2,789 (372 Mineralized) | 94 holes processed
Variogram Model | Spherical (Isotropic) | Experimental variogram fit
Nugget / Sill / Range | 18.81 / 32.39 / 218 m | Scipy curve_fit
Avg Drill Spacing | 37.3 m | Nearest-neighbour distance
Suggested Block Size XY | 18.7 m (half spacing) | Industry rule of thumb
Suggested Block Size Z | 2.0 m | Matches composite length
Notes: All outputs exported as CSV files ready for direct import. Kriging and formal resource classification require a Qualified Person under JORC or NI 43-101.

## Slide 8
Conclusions & Recommendations
◆
Mineralization is hosted exclusively in QV1 and IN rocks (mean grades 4.1 and 9.2 g/t)
◆
Clear NE-SW structural trend (42.7°) with 86.5% confidence — focus future drilling here
◆
Ore shoot plunges gently SW at 12° — favorable for near-surface resource extension
◆
Spatial correlation persists to 218 m — current 37.3 m drill spacing is more than adequate
◆
MU rock (1.95 g/t mean) warrants reclassification into the Mineralized Domain
All geostatistical parameters exported and ready for import into Surpac, Datamine, or Leapfrog Geo.
Formal resource classification (Inferred/Indicated) requires a Qualified Person under JORC / NI 43-101.
Notes: End with the business impact: NE-SW drilling corridor, 218m search radius, MU reclassification recommendation.

## Slide 9
ملخص النتائج بالعربية
◆
التمعدن مرتبط حصرياً بصخور QV1 (العروق الكوارتزية) والصخر الجوفي IN
◆
الاتجاه الأساسي للتمعدن: شمال شرق - جنوب غرب (42.7°) بثقة 86.5%
◆
عمود التمعدن يميل بزاوية خفيفة 12° ناحية الجنوب الغربي
◆
أقصى مسافة ترابط مكاني: 218 متر — أساس تصميم Block Model
◆
الحد الأقصى للعيار المطبق: 60 g/t — يؤثر على 1% فقط من العينات الممعدنة
◆
صخر MU (متوسط عياره 1.95 g/t) مرشح لإعادة تصنيفه ضمن النطاق الممعدن
◆
تركيز الحفر الاستكشافي الجديد على امتداد محور الشمال الشرقي - الجنوب الغربي